## Slide 1: Zoom
All:-
This is used to present the full drawing in the present viewport.
Center:-
This is used to show a window defined by a center point and a magnification value or height. A lesser value for the height enlarges the magnification. A bigger value reduces the magnification.
Dynamic:-
It is used to show the generated portion of the drawing with a view box. The view box represents our viewport, which we can reduce in size or enlarge and move around the drawing. Positioning and sizing the view box pans or zooms to fill the viewport with the image inside the view box.
Extents:-
It is used to show the drawing extents and results in the largest possible display of all the objects.

## Slide 2
Previous:-
Zooms to display the previous view. You can restore up to 10 previous views.
 Window:-
Zooms to display an area specified by two opposite corners of a rectangular window.
 Real Time:-
Using the pointing device, zooms interactively to a logical extent. The cursor changes to a magnifying glass with plus (+) and minus (–) signs. Hold your mouse left button and move vertically to zoom in and move downward to zoom out.

## Slide 3: Scale

Zooms the display at a specified scale factor. Enter a value followed by x to specify the scale relative to the current view. For example, entering .5x causes each object to be displayed at half its current size on the screen. Enter a value followed by xp to specify the scale relative to paper space units. For example, entering .5xp displays model space at half the scale of paper space units. You can create a layout with each viewport displaying objects at a different scale. Enter a value to specify the scale relative to the limits of the drawing. (This option is rarely used.) For example, entering 2 displays objects at twice the size they would appear if you were zoomed to the limits of the drawing.

## Slide 4: Region
Type reg↵ for region. This is used to change lines (closed lines) into a single Polyline.

## Slide 5: Construction Line
This is used for multiple purposes like:-
· To draw horizontal, vertical or angular line.
· To draw offset (off set is used to draw the walls etc) and projections etc.
· To bisect an angle.
· To check a certain line for horizontal or vertical etc.
o Type XL↵
o Type H for horizontal or V for vertical line. We will see that a line of infinite length is drawn. Now we can use it for our required purposes like to check any line in our drawing etc.
o If you want angular line, Type XL↵ and then press A for angle. And then you will be asked to enter angle. Type the angle value and press↵. Here we can also press R to use a line as a reference.

## Slide 6: Chamfer
Using CHAMFER is a fast way of creating a line between two nonparallel
lines. It is usually used to represent a beveled edge on a corner. CHAMFER can also
be used to bevel all corners of a Polyline.
You can chamfer lines, Polylines, Xlines, and rays.
o Type cha↵
o (We will see different sub-options/commands which will be discussed later.)
o Now select the first line which is labeled as A in Fig16.
o After that we will be asked for second line. So select second line which is labeled as B in Fig16.
o We will see that the corner is chamfered (if you see no chamfering although in command window you can see that the command has been applied then you
have to change the chamfer settings which are described below in sub commands).